| TAPE Attachment Method Part Number: 375324B00035G (Vis Number: 035731) |
| --- |
| BGA Surface Tape Type Heat Sink Finish Plastic T411 Black Anodize |
| Features and Benefits • Tape mounting saves board space by eliminating mounting holes • Convenient peel and stick assembly is quick and clean • Pin Fin array allows omni-directional airflow to maximize heat dissipation |  |
| Width Length Height Fin Thickness Across Width Fin Thickness Across Length Base Thickness # of fins across width # of fins across length 10.2mm 10.2mm 10.2mm 1.57mm 1.27mm 1.57mm 4 4 |
| Mechanical Outline Drawing |
| Unless otherwise shown, tolerances are ±0.38(±.015) |
| Thermal Performance |
| *θn **θf 71.4 21.2 |

*Natural convection thermal resistance is based on a 75 °C heat sink temperature rise. **Forced convection thermal resistance based on an entering 1.0 m/s (200 lfm) airflow. Due to various heat dissipation paths within a BGA device, please test the heat sink in your application.